Unproto  Mode

One Station to Another

From one station to another type  unproto space and the station you are calling or talking to or you can also put CQ

Ie      UNPROTO KF6FIR (ENTER)   OR     UNPROTO CQ  (ENTER)

On the next line type conv  for converse mode.  After you press enter everything you type will be transmited out over the air waves without the need to connect directly to another station

To get out of converse mode hold down your ctrl key and press c then release them both.  Your command prompt will re-apear and type u id

Ie      U ID  ( ENTER)

_______________________________________________________________________

Digipeting through other nodes

To Digipeate through several nodes type   u name v node,node,node,node and press enter you are able to type up to 10 nodes in a row that has the potential to repete your signal hundreds or thousands of miles

IE     U ED V KOSO,KTUO,KBERR    (enter)

Now that you have told it witch nodes to go through type conv and enter

Ie      CONV  (ENTER)

To get out of converse mode hold down your ctrl key and press c then release them both.  Your command prompt will re-apear and type u id

Ie      U ID  ( ENTER)

Notes:

If you are using several local nodes to digipeate you will see your own words being transmitted back to you from the nodes you can hear.  Your signal will continue to go on past the nodes you can hear as long as you originally typed them in at the first step.   For a list of nodes visit               http://www.varmintal.net/ahamp.htm

A new node was just added in the west bay  wbay  is its name and you can reach it from koso.